## Slide 1: IKE-4 Training

## Slide 2: Agenda
IKE 4 – Introduction to IKE Field & IKE Office
Presentation
    Form Creation
    IKE Tools
    HOA’s
    Data Output
IKE 4 – Web demonstration of IKE Field
  Brief Video on Pole Data Collection
IKE 4 – Web demonstration of IKE Office
  Adding Fields to an IKE Collection Form
  Marking HOA’s in IKEphoto
  Data Output

## Slide 3: Introduction
Matthew Worster
Solutions Deployment Manager
matthew.worster@ikegps.com
720.323.2273
Jarrod Phillips
Support Engineer
Jarrod.Phillips@ikegps.com
406.274.4982

## Slide 5: Complete Solution

## Slide 6: Software Modules
Photo Measurement
Height
Width
Measurements are linked to real world objects
JSON, Print, KMZ, Excel
Standard Data Output
Pole Loading
SPIDACalc
PoleForeman
O-Calc Pro*
Form Design
Customizable
Multiple data collection option
3rd Party Pole Load Integration
Capture Tools
Photo Measure
Photo Only
Point to Point
Span Height
Target Position
Local Position
Nested / Sub-forms
Wireless Support
WiFi
Bluetooth 4.0
FME Cloud
Over 350 formats (.dwg, .shp, etc.)
IKE Field & Office
IKE Integration

## Slide 7: IKE 4 Generic Workflow

## Slide 8
Adding IKE Users

## Slide 9: IKE Office
Ability to modify forms/workflows & reports so the data is captured in the most productive method for your organizational needs.
Perform additional pole measurements from initial field measurements
Flexibility to import data and send updated forms directly to the field with Wi-Fi or hot spot Connection
Cloud-based software that allows for field data collection and analysis… your way!

## Slide 10: IKE Office (Login)
https://office.ikegps.com/#/login
Notes: Not sure if I am sold on the orange shadow box. Kind of indifferent I guess. Maybe smaller shadow if there’s nothing better

## Slide 11: Accounts Page (Add/Manage Users in Company Account)

## Slide 12: Adding User Accounts
Email address must be unique
Admin has ability to reset password and delete users
Pre-generated password will be given when user account is created

## Slide 13: Settings Screen (Change Passwords/Measurement Units)
Reset your password to something easily remembered
Username & password is used to login to IKE Field & IKE Office
Notes: Can we make the lines and the boxes show up at once for each segment. I.e. show the Username box with the line… then show the reset box with the line

## Slide 14
Creating IKE Forms & Workflows

## Slide 15: Work Flow Forms
What data should field teams collect?
Develop forms and workflow to support data needed
Create form within IKE Office software
When form is ready, deploy to IKE Device
Advance planning of all projects and identifying the exact data needed to support the end result, is very important to the success of a project using IKE. Forms should be developed to support the desired end-result!
Pre-planning is critical to ensure one trip to the pole!

## Slide 16: Forms Tab (Create Project Specific Forms)
New Form
Notes: Show line, circle and new form box at once

## Slide 17: Forms (Drag/Drop/Drop Functionality)
Label Field: Shows as Label in IKEphoto
Cloneable Field: Carries data into next pole added in IKE Field
Notes: Same here… show label field box and line… then show cloneable field box and line after

## Slide 18: IKE Tools
Text – Alphanumeric
Height – Span Height Tool (MidSpan and Vertical P2P Measurements)
    Allows for height tool use in field, manual data entry, or adding within IKEphoto in office
Photo Measure – IKEphoto (calibrated image)
List – Picklist
Nested List – Up to 3 Levels of Conditional Data
Subform – Allows for Grouping of Data
    Subform allows for multiple data items to be added in the field
Location – Target Position (laser) or Local Point (device)
Image – Image Only
Vector – Horizontal P2P Measurements (horizontal/slope/vertical distance & bearing)

## Slide 19: Deploy Form to IKE Field
Select Save once all items have been added to form
  Form is pushed to IKE Cloud
Login to IKE Field on Device
  Select form tab
  Download available form – Wi-Fi connection or mobile hot spot

## Slide 20
Introduction to IKE Field Tools

## Slide 21: IKE Field
An Android mobile app can be downloaded on the IKE Device (via Google Play Store – search for “IKE Field”). The app contains general measurement tools for field data collection and specialized utility pole measurements for:
    Heights
    Span lengths
    Attachment points
    GPS location
Notes: Need a picture of the IKE4 device and not a cell phone.

## Slide 22: Android Settings
Set Location to:
  Device Only
  SBAS On
Notes: Ike device instead of cell phone

## Slide 23: IKE Field (App Navigation)
Forms
Settings
Notes: Ike device instead of phone. Bring in boxes/lines one at a time

## Slide 24: IKE Field (Settings & Forms)
Notes: Ike device instead of phone.

## Slide 25: Compass Calibration (Once/Week)
https://ikegps.com/ike-4-compass-calibration/
Select START and follow instructions
Notes: Ike device instead of phone.

## Slide 26: IKE Tools
Location
IKEphoto
    Photo Measure
Height
Vector
Bearing
Measurement | Industry Requirement | Description | IKE 4 Accuracy
GPS Points | Sub Meter | Latitude, Longitude | Sub Meter CEP
Height Above Ground (HAG): Pole Height Height of Attachment (HOA): Wire, Equipment Attachment Height | +/- 2” | Measured on IKEphoto | +/- 2”
Span Length | +/- 24” | Measured in the field between poles known as a span | 1.5% of distance
Line Angles | +/- 5° | Compass bearings measured in the field of Conductor/Cable Tap Span, Service Drop (reference true geodetic North) | +/- 5°
Anchor/Guy Lead Length | +/- 6” | Measured in the field from face of pole to anchor in-ground point | 1.5% of distance
Mid-Spans HAG | +/- 2” | Measured in the field | +/- 2”

## Slide 27: Location
Target Position
    Calculated from Device GPS & Laser Target
Local Point
    GPS reading from the Device Location
  30-second countdown
Note: Location needs to be set to Device Only and SBAS on
Target Position
Local Point
Target Position
Local Point

## Slide 28: Location Tool (When to Use)
Local Point:
    Use when you can conveniently position the device at the exact location to be measured
    Avoid laser and compass error by taking device GPS reading
Target Position:
    Use when the location is not easily accessible, such as behind a fence, across a creek, etc.
    Target position is calculated using GPS coordinate, laser distance reading, and compass reading. It is less accurate than Local Point

## Slide 29: IKEphoto (Photo Measure)
Calibrated Photo
Measure Heights of Attachment in the Office
Edit/Add Missing Data
Target the Laser on the Pole
Line up Vertically with the Tip of the Pole
Attachment Points are on the “Face of the Pole”
IKEphoto

## Slide 30: IKEphoto (Laser)
The laser needs to be centered on the pole itself
Do not target the laser on any piece of equipment (riser) or other attachments
Pay attention to the Distance Indicator below the target
Ensure that you have the correct distance from the device to where the laser is hitting on the pole
Distance Indicator

## Slide 31: IKEphoto (Angles)
Use Base Offset Stick
    Known Reference Height
    Flat (butted up) against pole
Take from Multiple Angles
    See attachment points on “Face of the Pole”
Adjust for Multiple Brightness Levels

## Slide 32: Height Tool
Vertical P2P Measurements
    Height of Attachments
    MidSpan Measurements
Arrows give you estimated Ground Reference Point
Gather Measurements Safely
    No Touching Power Lines
    Good for Road Clearances
Height Tool
Manual Edit
Height

## Slide 33: Height Tool (Appropriate Condition)
The Height tool can produce accurate span height measurements when:
  There is no environmental interference to the target
      For example, there should not be vegetation around the wire. Ideally, the wire to be measured is in a clear sky backdrop
  There are no large structures such as building in close proximity of the wire
  The ground is free of obstacles including grass or snow
      Concrete ground would be an ideal situation

## Slide 34: Height Tool (Best Practices)
Eliminate any large angles
Pay close attention to the Distance indicator to ensure that you are hitting the wire
    Point A is the wire, and Point B will be the Ground (90 degrees) below the wire
    The arrows directing you should disappear when you are directly below the wire

## Slide 35: Vector Tool
Horizontal P2P Measurements
    Slope Distance
    Horizontal Distance
    Vertical Distance
    Bearing
Used for:
    Clearances
    Angles
    Span Lengths
    Anchor Lead Lengths
Vector

## Slide 36: Vector Tool (Best Practices)
Choose a common point on both of the poles to take the horizontal distance
    Use Communication to Communication Attachment Point, or Secondary to Secondary
    Avoid using the Base of one pole to the Tip of the Other
    Anchor Lead Lengths from the Inside Base of the Pole to where the Anchor is in the ground
Take the measurements as perpendicular to the wires as possible
Point A is always the pole that you are performing the inventory
    Point B will be the other pole
    Bearing is calculated from Point A to Point B
Pay attention to the Distance indicator to ensure that the laser has a good reading on the pole

## Slide 37: Vector Tool (Where to Measure)
A
A
B
B
GOOD
BAD
B
A

## Slide 38: Bearing Tool
Capture Equipment Bearing as it comes off the Pole
Directly face the Piece of Equipment
    Target Laser on Equipment
Rotates Bearing
    180 degrees
Bearing Tool
Bearing Tool

## Slide 39
Completing Measurements in IKE Office

## Slide 40: Process to Complete Measurements
Upload Field Data
To IKE Office via
Wi-Fi
Open Job in IKE Office
Open IKEphoto and use software to complete measurements

## Slide 42: Jobs Screen

## Slide 43: Collections Screen

## Slide 44: Photo Measure Screen

## Slide 45: Editing Data
Select On Item – Same Subforms in IKE Form

## Slide 46: Editing P2P Measurements
Manually Type In:
  Length (ft./in.)
  Bearing

## Slide 47: Copy From Existing Span
Data from 1st Span carried over in Mobile Device when “Cloneable” selected in IKE Form
Data labeled as ‘Fore’ or ‘Other’ on previous pole carried over in Office to ‘Back’ span of current pole

## Slide 48: The BIG Map (View All Jobs)

## Slide 49
Data Output

## Slide 50: Data Output Formats
KML
EXCEL
JSON (API)
IKE Report (PDF)
Image Zip (per pole)
Pole Loading
    SPIDACalc (JSON)
    OCALC Pro (LCANX)
    PoleForeman (JSON)

## Slide 51: Selective Outputs (Per Pole, Selection of Poles)
To output individual poles or a selection of poles to the above formats, access the collections via the Jobs tab.
Once a Job has been selected, choose the individual collection by selecting the CheckBox next to the left of that selection.
    Select the output ICON and choose the appropriate format
Individual Collection Checkbox

## Slide 52: Output Entire Job
Output entire job directly from the MAP, Photo Measure Screen, or by selecting ALL collections in Collections Screen.

## Slide 53: Output Multiple Jobs (Map Screen)
Select Multiple jobs for Output
Select Checkbox and Output Icon

## Slide 54: Excel Output
Subforms will create individual Tabs
Excel Output Export

## Slide 55: KML Output (Google Earth)
KML Output Export

## Slide 56: IKE Report
IKE Report Export